## Slide 1
Yue Qi
Third Year Ph.D. Stuent
Supervisor: Prof. Jin Yang
James Watt School of Engineering
University of Glasgow
Research Evolution and Integrated Framework for A Forecast-Driven Multi-Objective Optimisation Framework for Multi-Energy Systems

## Slide 2: Initial Research Focus: V2G Flexibility for Active Distribution Networks
The original PhD proposal focused on coordinating Active Distribution Networks (ADNs) with Vehicle-to-Grid (V2G) resources. As electric vehicles increase electricity demand and create new network constraints, V2G offers a way to transform EVs from passive loads into distributed flexibility resources.
The initial aim was to model EV user behaviour, forecast the temporal and spatial availability of V2G capacity, and optimise ADN operation to accommodate higher EV/V2G penetration without excessive network reinforcement.
How can EV/V2G flexibility be modelled and coordinated to support low-carbon, cost-effective, and flexible distribution network operation?

## Slide 3: Key Insight: V2G as a System-Dependent Flexibility Resource
V2G operation cannot be determined by EV behaviour alone. Its value and feasibility depend on wider system conditions, including local demand, renewable generation, electricity prices, carbon signals, network constraints, and user requirements.
This means V2G is not an isolated transport–grid interface problem, but a time-coupled and uncertain flexibility resource embedded within a broader energy system.
Research transition: From V2G-specific ADN optimisation to Multi-energy system level flexibility coordination and system optimisation.

## Slide 4: Integrated Research Framework: From V2G to Forecast-Driven MES Optimisation
The recent research is not a change of topic, but a progressive expansion of the same core problem: how flexible resources can be modelled, predicted, and optimised within increasingly complex energy systems.
V2G Flexibility for ADN (The original PhD proposal)
A Forecast-Driven Multi-Objective Optimisation Framework for Multi-Energy Systems
Future Work: Complex engineering scenarios with the high-performance algorithm
Stage 2: Reliable Long-Term Forecasting Input
Stage 1: MES Modelling and Optimisation
Engineering Extension: LVOE project - practical LVAC case study
Research Framework
Expected Outcome
How to realise

## Slide 5: Research Outputs Supporting the PhD Framework
Stage 1: MES Modelling and Optimisation
The first-stage work developed an Energy Hub simulation and multi-objective optimisation framework using an improved intelligent algorithm.
“A new model of energy hubs and multi-objective optimisation for future net-zero distribution networks,” 22nd IET International Conference on AC and DC Power Transmission (ACDC Global 2025), Birmingham, UK, 2025, pp. 313–319. doi: 10.1049/icp.2025.1224. Best Poster Award.
Stage 2: Generative AI-Based Long-Term PV Forecasting
The second-stage work developed a generative AI-enhanced hybrid forecasting framework for reliable long-term PV forecasting, serving as the forecasting engine for the PhD framework.
“A Generative AI-Enhanced Hybrid Framework for Reliable Long-Term Photovoltaic Power Forecasting,” Energy and AI, IF 9.6, accepted for publication.
Engineering Extension: LVOE Project
In parallel, the LVOE project provided engineering validation through LVAC network modelling, protection analysis, voltage-unbalance optimisation, and AI-based fault diagnosis. This work was developed in collaboration with Scottish Power Energy Networks. Main outputs include LVAC overcurrent protection review, Voltage-unbalance optimisation, Energy Hub operation and protection analysis, and AI-driven LVAC fault diagnosis.
“Protection insights from optimal operation of offshore energy islands under extreme weather conditions,” 19th IET Conference on Developments in Power System Protection (DPSP Europe 2025), Bilbao, Spain, 2025, pp. 240–245. doi: 10.1049/icp.2025.1076.
“Improved Fault Diagnosis for Intelligent LVAC Network Protection,” CIGRE Paris Session 2026, Full Paper accepted.

## Slide 6: Stage 1: MES Modelling and Optimisation
Fig.1 Illustration of the constructed EHs model representing an Eco-friendly Industrial Park:
overall multi-energy system structure;
detailed configuration of the CCHP subsystem.
Research Role: Provides the core modelling and validates the effectiveness of the improved intelligent algorithm for MES Multi-Objective optimisation.
(a)
(b)
“A new model of energy hubs and multi-objective optimisation for future net-zero distribution networks,” 22nd IET International Conference on AC and DC Power Transmission (ACDC Global 2025), Birmingham, UK, 2025, pp. 313–319. doi: 10.1049/icp.2025.1224.

## Slide 7: Stage 1: Solutions and Methods
The Energy Hub optimisation problem was formulated with three objectives: Operating cost, Carbon emissions, and System reliability.
Where carbon emissions are considered based on direct emissions during system operation rather than a full lifecycle assessment. System reliability is evaluated through the Load Energy Shortage Percentage (LESP).
Problems
In multi-objective optimisation problems, different objectives often conflict, meaning a single solution cannot intuitively reflect the trade-offs between objectives.
Decision-makers' preferences and other variations will directly impact the optimisation outcomes.

## Slide 8: Stage 1: Solutions and Methods
An improved MOGWO was developed by combining Pareto-based search, improved convergence control, mutation operation, and fuzzy decision selection.
The output is not a single deterministic solution, but a set of Pareto-optimal strategies for different decision preferences.
Pareto Front
In multi-objective optimisation, the Pareto Front is the set of all Pareto-efficient solutions. These solutions represent the best trade-offs among multiple objectives, meaning that no objective can be improved without deteriorating at least one other objective.
Fig.3 An example of a Pareto front.
Multi-Objective Grey Wolf Optimiser (MOGWO)
MOGWO simulates the structure of a wolf pack for optimisation and mimics grey wolves’ three main hunting phases: encircling, hunting and attacking prey, to find the global optimum solution.
Fig.2 The social hierarchy of a pack of grey wolves.

## Slide 9: Stage 1: Case Study and Key Findings
The Energy Hub model was tested on an 18-bus distribution network with bidirectional interaction with the upper-level electricity grid through power purchasing and selling. Three predefined operating scenarios were analysed: standard day, summer day, and winter day, with a fixed-schedule fuel cell bus included to represent transport-related hydrogen demand.
To test the decision-support capability of the improved MOGWO, three stakeholder preference settings were considered: Government (GOV), Operators (OPE), and Residents (RES). GOV prioritises carbon reduction, OPE balances carbon emissions and reliability, while RES prioritises cost minimisation.
The results show that the improved MOGWO produced well-distributed Pareto solutions and captured the trade-off among cost, carbon emissions, and reliability across different seasonal scenarios and stakeholder preferences.
Scenario | User | Cost (RMB) | Carbon Emission (kg) | LESP (%)
Standard | GOV | 109110.36 | 7903.81 | 4.77
 | OPE | 109617.69 | 8051.84 | 4.70
 | RES | 109110.36 | 7903.81 | 4.77
Summer | GOV | 114366.13 | 10737.66 | 8.25
 | OPE | 115939.26 | 10999.52 | 7.76
 | RES | 114167.15 | 10720.92 | 8.37
Winter | GOV | 121975.91 | 10638.00 | 4.50
 | OPE | 122430.50 | 10733.20 | 4.41
 | RES | 121294.64 | 10600.28 | 4.80
(1) MES Modelling and Validation√ (2) Algorithm Improvement √
Fig.4 Pareto Front for the summer scenario with demand response

## Slide 10: Key Transition: From Optimisation Engine to Forecast-Driven Decision-Making
Stage 1 established a workable optimisation engine for MES operation, but it also revealed a more fundamental issue: an optimisation model is only as useful as the inputs that drive it.
In the current Energy Hub framework, renewable generation, demand profiles, electricity prices, and operating conditions are treated as known inputs. This is reasonable for analysing historical or representative operating scenarios, but it limits the model to answering a short-term question: how should the system operate under given conditions?
For long-term planning, the key question is different: how should the system operate when future renewable generation, demand, prices, and flexibility availability are uncertain? This is especially important for MES, V2G, storage, and demand response, because their value depends on future system states rather than historical averages.
Therefore, the research naturally moves from building an optimisation engine to constructing reliable future inputs for that engine. This transition leads directly to Stage 2: forecast-driven optimisation under uncertainty.
“A Generative AI-Enhanced Hybrid Framework for Reliable Long-Term Photovoltaic Power Forecasting,” Energy and AI, IF 9.6, accepted for publication.

## Slide 11: Stage 2: Motivation
For MES planning, key optimisation inputs such as renewable generation, load demand, and operating conditions need to be forecast before future decisions can be made. However, these future system states are uncertain, and detailed future-year meteorological variables are not available in advance. This creates a major limitation for recent high-accuracy forecasting models, because most of them depend on observed or concurrent weather inputs that cannot be accessed in real year-ahead planning.
High temporal resolution is also essential. MES planning does not only require monthly or daily energy estimates; it also needs detailed profiles that capture intra-day variability, ramping behaviour, storage operation requirements, and demand interactions. Without this resolution, flexibility needs may be underestimated, and system planning results may become biased.
Therefore, the recent Stage 2 work develops a Generative AI-enhanced forecasting pipeline to construct 15-min year-ahead meteorological inputs and convert them into PV power forecasts. This provides reliable future renewable inputs for the next step of forecast-driven MES optimisation.
“A Generative AI-Enhanced Hybrid Framework for Reliable Long-Term Photovoltaic Power Forecasting,” Energy and AI, IF 9.6, accepted for publication.

## Slide 12: Stage 2: Step 1 Generative Year-Ahead Meteorology (YAM)
Conditional Time GAN
Yearly dataset and Pre-processing
LLM-Based Climatic Trend Refinement
Generative YAM
Physical Realism and Privacy-aware Check
The first step constructs Generative YAM to replace unavailable future meteorological inputs for long-term PV forecasting.
After pre-processing yearly PV and meteorological data, CTimeGAN generates high-resolution future weather sequences while preserving local seasonal and weather-dependent characteristics.
An LLM-based climatic trend refinement module further adjusts the synthetic sequences using coarse future-year climatic estimates and online reasoning.
The final Generative YAM is statistically consistent, physically plausible, future trend-aware, and privacy-aware, making it a reliable input for PV forecasting and later forecast-driven optimisation.

## Slide 13: Stage 2: Step 2 Forecasting Model and Intelligent Hyperparameter Optimisation
Enhanced Alpha Evolution Optimiser
Transformer-LSTM Model
Year-ahead PV power output with a resolution of 15 minutes
Fig.5 Architecture of the baseline Transformer–LSTM
Automatic hyperparameter searching

## Slide 14: Stage 2: Case Study and Key Findings
Case | Model | R² | MAE (kW) | RMSE (kW)
1 | Transformer–LSTM no Generative YAM | 0.5737 | 0.6535 | 1.1140
2 | Transformer–LSTM CTimeGAN YAM | 0.7568 | 0.5425 | 0.7997
3 | Transformer–LSTM Generative YAM | 0.7787 | 0.4971 | 0.7629
4 | Transformer–LSTM EAEO Generative YAM | 0.8031 | 0.4835 | 0.7196
Fig.6 Model performance comparison
The proposed framework was further validated across two PV sites, namely the main 150 kW Ningxia PV plant in China and the external 6 kW DKASC site in Alice Springs, Australia; the DKASC results show that, the proposed pipeline achieved the best performance, reducing RMSE by approximately 35% compared with the baseline.
Overall, the proposed method converts unavailable year-ahead future weather information into reliable high-resolution renewable generation inputs for MES optimisation in future work.

## Slide 15: LVOE Contributions: From Operation Analysis to Intelligent Protection
The LVOE project provides an engineering extension of the main PhD framework using practical LVAC network data provided by SPEN. Although it is not the core thesis stage, it is methodologically aligned with the main research, as both focus on complex distribution network modelling, optimisation, system uncertainty, and decision support. The project forms a complete engineering chain for modern LVAC networks:
Protection problem identification: identified the limitations of conventional overcurrent protection under distributed generation, bidirectional power flow, and dynamic fault-current behaviour.
Operation–protection coupling analysis: demonstrated through an offshore energy island case that extreme weather and optimised operation can reshape power flows and increase protection risk, highlighting the need for future AI-based overcurrent protection methods.
Hardware-based operation optimisation: investigated three types of devices for three-phase voltage-unbalance mitigation, improving the understanding of hardware-based LVAC operation optimisation.
Data-driven intelligent protection: developed a hybrid deep learning model for LVAC fault detection and classification, extending the work towards intelligent protection.
Key insight:
Modern distribution networks require integrated modelling, optimisation, and intelligent protection methods.
“Protection insights from optimal operation of offshore energy islands under extreme weather conditions,” 19th IET Conference on Developments in Power System Protection (DPSP Europe 2025), Bilbao, Spain, 2025, pp. 240–245. doi: 10.1049/icp.2025.1076.
“Improved Fault Diagnosis for Intelligent LVAC Network Protection,” CIGRE Paris Session 2026, Full Paper accepted.

## Slide 16: Conclusion: A Coherent PhD Research Trajectory
The research started from V2G-specific ADN optimisation and was progressively abstracted into a broader problem of flexibility coordination in complex energy systems. In this process, the work evolved from local V2G operation towards multi-energy system-level coordination and optimisation.
Stage 1 established the Energy Hub-based MES optimisation framework and provided the core optimisation engine. At the same time, it revealed a key limitation: optimisation performance strongly depends on future system inputs, such as renewable generation, demand profiles, and operating conditions.
Stage 2 has recently addressed this input-side limitation by developing a novel framework for constructing reliable year-ahead, 15-minute PV power generation profiles. The next step will extend this forecasting capability to other critical inputs, such as wind generation and demand, and integrate these forecasts into the MES optimisation model to analyse their impacts on system operation and planning.
In parallel, the LVOE project validated the practical relevance of complex distribution network modelling, optimisation, and intelligent protection methods.
Overall, the PhD forms a coherent trajectory:
V2G flexibility → MES optimisation → Year-ahead forecasting and extension → Forecast-driven MES operation and planning.

## Slide 17: Future Work: From MES Optimisation to Complex Engineering Systems
Forecasting model extension: expand from PV forecasting to other key MES inputs, including wind generation, demand profiles, electricity prices, and operating conditions.
Forecast-driven MES operation and planning: integrate forecasted inputs into the MES optimisation model to assess impacts on cost, carbon emissions, reliability, storage scheduling, and demand response.
Complex engineering applications: test and enhance the framework under higher complexity, stronger uncertainty, and stricter operational requirements.
Target scenarios: extend from a single Energy Hub to multi-Energy Hub coordination and high-energy-demand infrastructures such as data centres.
Key direction:
Forecast extension → Forecast-driven MES optimisation → Real-world complex energy system decision support.

## Slide 18: Future Work: Data Centre Energy–Computation–Cooling Optimisation
A potential future application is data centre energy systems, where high electricity demand, intensive cooling needs, and strict reliability requirements create a more challenging optimisation scenario.
The problem would extend from traditional MES optimisation to Energy–Computation–Cooling coupled optimisation. IT workload affects power demand and heat generation, while cooling demand depends on both server load and ambient conditions.
The existing framework can be extended using generative scenario construction, uncertainty-aware forecasting, and intelligent optimisation to coordinate energy supply, workload scheduling, and cooling control.
Expected outcome:
low-carbon, reliable, and flexible data centre operation.